CORRIGENDUM No: 1

to the

CONTRACT NOTICE

Publication Ref: HUSRB/1203/111/049-works

Subject: Rehabilitation of cross-border connecting road Bácsalmás-Bajmok between Bácsalmás and the State Border

Location – Bács-Kiskun County/Hungary

The following alterations and/ or corrections are made to the Contract Notice:

16. Selection criteria

The former text:

1. Economic and financial capacity of candidate:

(a)	the average annual turnover of the candidate in the past three years (2011, 2012 and 2013) must exceed the amount of EUR 800,000;

2. Technical and professional capacity of candidate:

(a)	has at least one employee with a minimum 3-year professional practice in managing road construction works and with the qualifications necessary to obtain the licence listed as “MV-KÉ” as specified in the Government decree 266/2013 (VII.11.) or having this or equivalent licence in the register of the Hungarian Chamber of Engineers.

(b)	has completed (the taking-over certificate is issued) at least one contract in the field of road rehabilitation works which was fulfilled in a national public road with the overall length of at least 1 km, within a period of five years before the deadline for submission of tenders.

The Contracting Authority reserves the right to ask for copies of certificates of the taking over certificate / final acceptance signed by the supervisors/contracting authority of the project concerned. (This means that the project the tenderer refers to could have been started/implemented/completed at any time during the indicated period but it does not necessarily have to be started and completed during that period, nor implemented during the entire period.);

(c)	has at least one level controlled asphalt finisher.

(d)	if it is a sole tenderer it must carry out at least 70 % of the contract works using its own resources, which means that it must have the equipment, materials, human and financial resources necessary to carry out that percentage of the contract.

(e)	if it is the lead member of a joint venture/consortium, it must be able to carry out at least 50 % of the contract works using its own means.

If a tender is submitted by a consortium, unless specified, the selection criteria listed above will be applied to the consortium as a whole.

Shall read as new text:

1. Economic and financial capacity of candidate:

(a)	the average annual turnover of the candidate in the past three years (2011, 2012 and 2013) must exceed the amount of EUR 800,000;

2. Technical and professional capacity of candidate:

(a)	has at least one employee with Msc or Bsc qualifications on the field of the technical sciences and with a minimum 36 month professional experience -gained after having the required qualifications-  in the project management of public road construction works and who shall act as project leader during the completion of the contract. The completion of the contract shall only be commenced when this project leader will have obtained the licence marked “MV-KÉ” according to the Government decree 266/2013 (VII.11.) or the “MV-KÉ/A” according to the 244/2006 (XII.) Government decree (or equivalent licence) and listed in the register of the Hungarian Chamber of Engineers as so..

(b)	has completed and ended -in accordance with the prescriptions of the relevant contracts- road construction works in national roads with the lengths of min. 1,0 km in the field of construction of new sections or widening to four-lane-road or road pavement rehabilitation/reinforcement works within the period of five years before the deadline for submission of tenders.

This means that the taking-over certificates of projects the tenderer refers to must have been issued within the indicated period.

The Contracting Authority reserves the right to ask for copies of certificates of the taking over certificate / final acceptance signed by the supervisors/contracting authority of the project concerned. ;

(c)	has at least one level controlled asphalt finisher.

(d)	if it is a sole tenderer it must carry out at least 70 % of the contract works using its own resources, which means that it must have the equipment, materials, human and financial resources necessary to carry out that percentage of the contract.

(e)	if it is the lead member of a joint venture/consortium, it must be able to carry out at least 50 % of the contract works using its own means.

If a tender is submitted by a consortium, unless specified, the selection criteria listed above will be applied to the consortium as a whole.

____

All other terms and conditions of the Contract Notice remain unchanged. The above alterations and /or corrections to the Contract Notice are integral part of the Contract Notice.